## Slide 1
This pinout is valid for firmware fw-vXX1 or fw-vXX2 only
Arduino Leonardo (as wheelbase) -> Arduino Nano or UNO (as button box)
Leonardo GND -> Nano GND
Leonardo 5V -> Nano 5V
Leonardo pin 6 (DT_sh) -> Nano pin 12
Leonardo pin 7 (CLK_sh) -> Nano pin 13
Leonardo pin 8 (PL_sh) -> Nano pin 10 and pin 2
Nano pins available for buttons (16 max):
A0, A1, A2, A3, A4, A5, TX1, RX0, 3, 4, 5, 6, 7, 8, 9, 11
Goes in the wheel rim along with all switches
Up to 16 switches are possible (can be less or none)
one pin of each switch go to one of these pins,
other end of all switches go to GND
when pressed, switch has to short these 2 pins (normally open contact)
you will need to find a way to take
5 wires through or around the wheel shaft
separate button box
*.ino file is provided